## Slide 1
OBJECT DETECTION USING OPENCV WITH ROS2 AND TURTLEBOT4

## Slide 2
INTRODUCTION
  This project explores the integration of real-time object detection into a mobile robot system.
  Utilized ROS2 Humble, OpenCV, and YOLOv8 to achieve perception tasks.
  Platform used: TurtleBot4 with integrated RGB-D camera and LiDAR. Rviz for vizualization.
  Application: Indoor robotic navigation and intelligent decision-making in dynamic environments.

## Slide 3
PROBLEM STATEMENT
  Mobile robots often lack robust perception in dynamic indoor environments.
  Real-time detection of obstacles and semantic objects is critical.
  Manual control or basic obstacle avoidance is inefficient.
  Our goal: Enable a robot to autonomously navigate and identify objects like people, furniture, and devices.

## Slide 4
OBJECTIVES
  Deploy a real-time object detection pipeline on TurtleBot4 using YOLOv8 and OpenCV.
  Integrate the detection results with ROS2 navigation and SLAM for autonomous movement.
  Create a reliable system for detecting multiple classes of objects in real-world environment.

## Slide 5
BORCELLE
Contact
About Us
Service
Home
SYSTEM ARCHITECTURE
  Hardware: TurtleBot4, LiDAR, RGB-D Camera, onboard compute (Raspberry Pi 4).
  Software Stack:
    ROS2 Humble middleware
    OpenCV for image processing
    YOLOv8 for object detection
    RViz2 and Foxglove Studio for visualization
  ROS2 Nodes:
    Camera publisher
    Detection processor (Python Node)
    Navigation stack (Nav2)

## Slide 6
WIFI SETUP
  TurtleBot4 comes with a default hotspot:
    SSID = TurtleBot4-XXXX
  On your computer, connect to the TurtleBot4 hotspot via Wi-Fi settings.
  Once connected, open a terminal and use:
  ssh ubuntu@turtlebot4.local
  Password is usually ubuntu
  This enables direct communication without needing additional Wi-Fi configuration.

## Slide 7
NAVIGATION STACK SETUP
  Installed turtlebot4_navigation and nav2_bringup packages.
  Performed initial mapping using slam_toolbox in synchronous mode.
  Saved map using ros2 run nav2_map_server map_saver_cli.
  Launch navigation with:
    ros2 launch turtlebot4_navigation navigation.launch.py map:=/path/to/map.yaml
  Used RViz2 to set goals and observe real-time path planning.
  Detection topics influence path re-evaluation for dynamic obstacle avoidance.

## Slide 8
DATASET AND MODEL TRAINING
  Data Collection: Captured RGB images of the lab environment.
  Classes: Over 60 general and lab-specific indoor objects (e.g., laptops, chairs, 3D printers, markers, bottles, bags).
  Annotation Tool: LabelImg and Roboflow.
  Model Training:
    Framework: Ultralytics YOLOv8 (Nano variant for performance) and CUSTOM data
    Epochs: 100
    Batch Size: 16
    Optimizer: AdamW
    Evaluation: mAP@0.5 = ~92%

## Slide 9
DATASET AND MODEL TRAINING
Key Components:
  Libraries Used: rclpy, sensor_msgs.msg.Image, ultralytics.YOLO, numpy, OpenCV
  Model: YOLOv8n.pt – optimized for speed (~10 FPS on Raspberry Pi 4)
  Subscribed Topic: /oakd/rgb/preview/image_raw – camera feed
  Filtered Detection: Only detects objects from predefined allowed class list with known physical widths
Workflow:
  Image Conversion: Converts ROS2 image messages to OpenCV BGR frames.
  YOLOv8 Inference: Performs prediction with confidence > 0.5.
  Class Filtering: Matches detected labels with allowed classes (e.g., chair, bag, laptop, person).
  Visualization: Draws bounding boxes and confidence scores using cv2.rectangle() and cv2.putText().
  Logging: Detected class and coordinates logged to console.

## Slide 10
IMPLEMENTATION IN ROS2
  Used CV Bridge to convert ROS image messages to OpenCV format.
  Processed frames through YOLOv8 model.
  Published detected objects to a custom ROS2 topic.
  Integrated detections into Nav2 behavior tree for basic obstacle reasoning.
  SLAM Toolbox used to create map of the lab environment.

## Slide 11
CHALLENGES AND SOLUTIONS
  Latency in inference: Solved by using YOLOv8n variant.
  Lighting variability: Augmented dataset with brightness/contrast changes.
  Camera calibration issues: Used ROS2 camera_info_manager to fix intrinsics.
  Integration with Nav2: Resolved with behavior tree customization.

## Slide 12
RESULTS
Demonstration Video

## Slide 13
RESULTS
FIG 1 : Real time vizualization of robot in the environment.

## Slide 14
CONCLUSION
  Successfully built an intelligent perception system using ROS2 and TurtleBot4.
  Real-time object detection and SLAM integration achieved.
  Future Directions:
    Deploy object tracking (Deep SORT or ByteTrack).
    Run model inference on edge AI hardware (e.g., Jetson Xavier).
    Improve semantic reasoning for navigation.

## Slide 15
Gunjay Suhalka (22070127022)
Manan Khatri (22070127034)
Sahran Altaf (22070127059)
Yash Golani (22070127072)
PRESENTED BY
Dr. Manoj Kumar Shukla
Professor
Department of Robotics and Automation
SUBMITTED TO
THANK YOU